## Slide 1
LUTES Deep Tech Hackathon 2026 · Challenge 1
Obstacle-Avoiding Rover
A 2WD robot that measures the distance to obstacles and drives around them on its own
Caspian Mavericks
Mohammadsadegh Shoushtaridehshal
Amirmohammad Shariatkhah

## Slide 2: 1 Challenge and what we built
The brief
“Design and construct a mobile two-wheel drive (2WD) robotic rover capable of navigating dynamic environments autonomously by measuring distances to surrounding obstacles and executing avoidance maneuvers to prevent collisions.”
Our rover
Measures the distance ahead every 60 ms
Stops at 20 cm, reverses, scans 7 directions
Curves towards the clearer side
Remembers where it has already driven
Detects when it is stuck on something it cannot see
Live dashboard over WiFi: radar, map, manual control

## Slide 3: 2 Hardware
Part | Why
Arduino UNO R4 WiFi | Controller with built-in WiFi for the dashboard
2 × 28BYJ-48 steppers + ULN2003 | Every step is counted: exact distance and turn angle. The kit had no driver for DC motors
HC-SR04 on SG-90 servo | One sensor scans from 60° to 120°
2 × 18650 + switch → VIN | 7.4 V; the board's regulator feeds the 5 V rail

## Slide 4: 3 Obstacle avoidance
Drive
Measure ahead every 60 ms
Detect
Under 20 cm, confirmed by a second reading
Back off
Reverse 15 cm
Scan
7 directions, 60° to 120°, median of 3 readings
Turn
45° curve, 25 cm radius, to the better side
Better side = free space measured on that side − 20 cm for every already-visited cell the curve leads into
Both sides blocked → reverse along a curve and scan again; no spinning in place
Motors run from a 10 kHz timer interrupt → measuring and WiFi never pause the wheels

## Slide 5: 4 Position, memory and stuck detection
Our chair test track
Position from the steps
x, y and heading from the step counts of both wheels (4096 half-steps per wheel turn). No extra sensor needed.
Memory of visited places
10 cm grid over 6 × 6 m. On the chair track the robot kept turning back to the entrance; now turns that lead into visited cells lose points.
Stuck detection
Steppers give no feedback. If the steps say 10 cm but the distance ahead changed less than 3 cm, something the sensor missed (a thin chair leg) is blocking it: back off and turn.

## Slide 6: 5 Dashboard
Shown with test data
Served by the robot itself: http://192.168.137.50
START / STOP and hold-to-drive arrows
Speed sliders, applied live
Radar: the last 7-point scan
Map: path and detected obstacles
Distance graph and event log
Manual drive stops by itself at 20 cm and when the signal is lost

## Slide 7: 6 Testing and calibration
Calibration
Test | Result
Drive 30 cm | Drove 34 cm → wheel diameter 6.8 cm
Spin 360° | Turned 340° → wheel distance 21.6 cm
Speed steps 900 to 1700 | 1500 skips steps → 1100 (5.7 cm/s)
Servo sweep | 60° to 120° free, 90° straight ahead
Problems found and fixed
Problem | Fix
Battery wired to the 5 V rail | Battery to VIN only
Robot never stopped | 30 ms pause before the confirming reading
Motors clicking | Lower speed, smooth acceleration
Hotspot gave no address | Fixed IP 192.168.137.50
Went back out of the U-track | Memory of visited cells
Thin chair legs not seen | Stuck detection

## Slide 8
Live demo
START from the dashboard
Obstacle ahead: stop, back off, scan, curve away
Radar and map update while it drives
Manual drive with the arrow keys, then STOP

## Slide 9: 7 Limitations and next steps
Limitations
Sees only ahead while driving (about ±15°)
Very thin or steeply angled objects can be missed
Map drifts when the wheels slip
Slow: about 5.7 cm/s with 5 V steppers
Next steps
Bumper switches on the front corners
Side sensors to follow walls
Geared DC motors with encoders for speed
Use the stored map to plan a route
Code: github.com/sadeghshoushtari/obstacle-avoiding-rover
Libraries used: AccelStepper, Servo, WiFiS3